## Slide 1
AI MINOR COURSE
Optimizing
Liquid-Liquid
Extraction
Using Artificial Neural Networks (ANN)
PRESENTED BY
A
Aditya
U24CH043
Y
Yatharth
U24CH045
A
Aryan
U24CH069
Department of Chemical Engineering
Academic Year 2025–2026

## Slide 2
AI Minor Course | Department of Chemical Engineering | 2025–2026
OVERVIEW
Presentation Agenda
01
Introduction to LLE
What is liquid-liquid extraction and why optimize it?
02
Artificial Neural Networks
Structure, training, and how ANN works
03
Case Study
Reactive extraction of itaconic acid using TOA & DCM
04
ANN Pipeline & Results
1,200 data points, R² = 0.9875, optimal conditions
05
Sensitivity Analysis
Which variables matter most?
06
Advantages & Limitations
What ANN does well and where it falls short
07
Future Directions
Digital twins, Hybrid Models (Mechanistic + ML), Reinforcement Learning (RL)

## Slide 3
AI Minor Course | Department of Chemical Engineering | 2025–2026
BACKGROUND
What is Liquid-Liquid Extraction?
Core Principle
A solute is transferred from an aqueous phase into an immiscible organic phase based on its relative chemical affinity for each phase.
Key Equations
Distribution Coefficient:
D = C_organic / C_aqueous
Extraction Efficiency:
%E = 100 × D / (D + Vaq/Vorg)
Key Process Variables
Acid / Solute Concentration
Controls the reaction stoichiometry
Extractant (TOA) %
Chemically binds to the target solute
Modifier (DCM) %
Improves organic phase solvation
Temperature (°C)
Affects reaction kinetics & viscosity
Phase Ratio (Vorg/Vaq)
Determines driving force for transfer

## Slide 4
AI Minor Course | Department of Chemical Engineering | 2025–2026
ARTIFICIAL NEURAL NETWORK
How Does an ANN Work?
Input Layer
5 neurons
Hidden Layer 1
15 neurons (tanh)
Hidden Layer 2
10 neurons (tanh)
Output
1 neuron
Acid
TOA%
DCM%
Temp
Ratio
...
%Y
Training loop: 1 Forward pass — predict %Y from inputs → 2 Compute error vs. actual experiment → 3 Backpropagation — assign blame to weights → 4 L-BFGS update — adjust all weights → 5 Repeat until RMSE is minimised

## Slide 5
AI Minor Course | Department of Chemical Engineering | 2025–2026
PS
Problem Statement
Liquid–liquid extraction involves complex nonlinear interactions between multiple process variables, making accurate modeling and optimization difficult using conventional methods. Artificial Neural Networks (ANN) can be used to predict and optimize extraction efficiency effectively.

## Slide 6
AI Minor Course | Department of Chemical Engineering | 2025–2026
CASE STUDY
Reactive Extraction of Itaconic Acid
TARGET SOLUTE
Itaconic Acid (IA)
Bio-based dicarboxylic acid from fungal fermentation. Used in adhesives, fibres, polymers.
EXTRACTANT
TOA (tri-n-octylamine)
Reacts chemically with IA to form organic-phase complex: HA + TOA ⇌ TOA·HA
MODIFIER
DCM (dichloromethane)
Improves solvation of extracted complex; prevents third-phase formation
OPTIMIZER
ANN + Differential Evolution
ANN trained on 1,200 data points; DE searches for max %Y automatically

## Slide 7
AI Minor Course | Department of Chemical Engineering | 2025–2026
PIPELINE & RESULTS
ANN Pipeline and Model Performance
Generate
1,200 Samples
Normalize
Inputs [0,1]
Train ANN
5→15→10→1
Validate
15% Test Set
Optimize
Diff. Evolution
R² = 0.9875
Test set accuracy
RMSE = 1.96%
Root mean sq. error
MAE = 0.60%
Mean absolute error
1,020 / 180
Train / Test split
Optimal Conditions Found by ANN + Differential Evolution
Variable | Range Tested | Optimal Value | Result
Acid Conc (mol/L) | 0.010 – 0.150 | 0.073 mol/L | Peak reaction stoichiometry
TOA Extractant (%) | 1 – 40 % v/v | 25.4 % | Near saturation point
DCM Modifier (%) | 10 – 100 % v/v | 90.0 % | Maximum solvation capacity
Predicted %Y | — | 89.95 % | Excellent extraction

## Slide 8
AI Minor Course | Department of Chemical Engineering | 2025–2026
SENSITIVITY ANALYSIS
Which Variables Matter Most?
High Impact
TOA Extractant %
Range: 1% → 40%
%Y swing:
78.6% → 99%
Strong positive effect. Extraction rises sharply until ~25%, then plateaus as extractant saturates.
High Impact
DCM Modifier %
Range: 10% → 100%
%Y swing:
75.3% → 99%
Monotonically increasing. DCM improves organic phase solvation. Plateau above 71%.
Narrow Optimum
Acid Concentration
Range: 0.01 → 0.15 mol/L
%Y swing:
Peak near 0.072
Narrow optimal window. Too low = insufficient substrate; too high = excess disrupts equilibrium.
Relative Variable Importance (% Y swing)

## Slide 9
AI Minor Course | Department of Chemical Engineering | 2025–2026
CRITICAL EVALUATION
Advantages & Limitations of ANN
ADVANTAGES
Universal approximator
Can model any nonlinear function — no equation assumed
Higher accuracy
R² = 0.9875 vs RSM's ~0.97 on same system
No prior knowledge
Learns from data alone — no thermodynamic params needed
Instant predictions
Millisecond inference after training; no new experiments
Couples with optimizer
Works with GA, PSO, or Differential Evolution for global optimum
LIMITATIONS
Black-box nature
Cannot produce explicit equation; hard to interpret physically
Data hungry
Needs 50–100+ training points; performance drops below this
Overfitting risk
Without regularisation, may memorise training data
No extrapolation
Only reliable within training data range; fails outside
Architecture tuning
Optimal layers/neurons must be found by trial and error

## Slide 10
AI Minor Course | Department of Chemical Engineering | 2025–2026
PHASE 2
Future Directions
Physics-Informed ANN
Combine thermodynamic laws (mass transfer, phase equilibrium) with ML, consistent predictions and better generalisations than ANN with less data
Reinforcement Learning
Learns optimal operating policies dynamically, Suitable for real-time process control and optimization.
Digital Twins
Virtual replica of extraction process, Enables real-time monitoring and predictive optimization, Combines simulation + AI + process data